## Slide 1: Measuring the Deployment of IPv6: Topology, Routing, and Performance
Amogh Dhamdhere, Matthew Luckie, Bradley Huffaker, kc claffy (CAIDA / UC San Diego)
Ahmed Elmokashfi (Simula Research)
Emile Aben (RIPE NCC)

## Slide 2: IPv6 Will Be Deployed Any Day Now
Amogh Dhamdhere, Matthew Luckie, Bradley Huffaker, kc claffy (CAIDA / UC San Diego)
Ahmed Elmokashfi (Simula Research)
Emile Aben (RIPE NCC)

## Slide 3: When will we run out of IPv4 addresses?
IANA runout
IANA ran out of IPv4 addresses in 2011
Regional Internet Registries (RIRs) are rationing but will soon run out too
3
Source: http://www.potaroo.net/tools/ipv4/index.html
Notes: 3

## Slide 4: IPv6
Address run-out was anticipated back in the 1990s
IPv6 was standardized in the late 90s
Operating systems and network hardware have supported IPv6 for many years now
IPv6 provides much more address space than our foreseeable need
4

## Slide 5: What’s the Problem?
Just use IPv6, right?
The issue: IPv6 is not backwards compatible with IPv4
  Hosts with an IPv4 address cannot directly communicate with hosts with IPv6 addresses
IPv6 configuration, management and troubleshooting still not well understood
5

## Slide 6: Growth of IPv[4|6]
IPv6 is here

## Slide 7: IPv6 growth: we need to zoom in..
The IPv6 topology grows exponentially while the IPv4 topology now grows linearly
Exponential
Linear
Exponential

## Slide 8: Digging deeper
Exponential growth of IPv6 is encouraging
  shift from a “toy” network to production?
Which geographical regions and network types contribute most of the growth?
Is the business mix in IPv6 converging to that in IPv4?
Is IPv6 performance comparable to IPv4 performance?

## Slide 9: Measurement Data
Topology snapshots+updates from BGP routing datasets from 1998-present
  Routeviews and RIPE
Annotated AS topology with business relationships on each link (Gao)
  TODO: Integrate CAIDA’s algorithm (in process)
Annotated ASes with
  Business types
    Transit, Content/Access, Enterprise, etc
  Geographical regions
    ARIN, RIPE, APNIC
Web page downloads and AS paths to dual-stack webservers in Alexa 1M (performance)

## Slide 10
AS Business Types
UCSD
Regional provider
Regional provider
Georgia Tech
Rapidshare
Comcast
AT&T
Level3
Verizon
Content/Access/Hosting Provider (CAHP)
Small Transit Provider (STP)
Large Transit Provider (LTP)
Enterprise Customer (EC)
$$$
$$$
$$$
$$$
$$$
$$$
p2p
p2c
A. Dhamdhere, C. Dovrolis. Twelve Years in the Evolution of the Internet Ecosystem. IEEE/ACM Transactions on Networking, vol. 19, no. 5

## Slide 11: Key Results
IPv6 deployment is strong in core, lagging at edge
Performance is similar between IPv6 and IPv4
  particularly with identical AS-level paths
< 50% of AS-level paths are identical
  But could be much larger without deploying any new infrastructure
  70% could be identical without establishing new peerings
  >90% could be identical by establishing equivalent peerings amongst existing IPv6-deployed ASes
Path exploration / convergence delay in IPv4 and IPv6 has been the same since 2008

## Slide 12: Evolution of the business mix
IPv6 deployment at the edges is lagging
IPv4 network is dominated by ECs
Lower fraction of ECs in IPv6
Hypothesis: As IPv6 matures, the business mix should become similar to that in IPv4

## Slide 13: Growth trends by geographical region
IPv6: RIPE region was always ahead of ARIN
IPv4: More ASes in RIPE region than ARIN since 2009
The ARIN region is lagging in IPv6 deployment

## Slide 14: IPv4 and IPv6 topology convergence
Transit providers and content providers are mostly present in the IPv6 graph, ECs are lagging
APNIC and RIPE lead ARIN in IPv6 presence
Classification: business type
Classification:
geographical region
IPv6 convergence is not uniform across business types and geographical regions

## Slide 15: Structure of AS-level paths
Hypothesis: As IPv6 matures, routing paths in IPv4 and IPv6 should become similar over time
Measured AS-level paths from 7 vantage points towards dual-stacked origin ASes
Focused on the fraction of identical IPv4 and IPv6 paths from each VP

## Slide 16: Identical AS-level paths
The fraction of identical paths is increasing
Currently less than 50% of IPv4 and IPv6 paths are identical
The IPv6 network is maturing, but slowly

## Slide 17: Comparing IPv4 and IPv6 performance
Poor performance over IPv6 is likely to inhibit the adoption of IPv6
How often is performance over IPv6 similar to that over IPv4?
Measurements from 5 dual-stacked vantage points (CAIDA Ark) to dual-stacked websites
  Webpage download times
  AS paths to those websites (traceroute)

## Slide 18: Performance: Webpage downloads
79% of paths had IPv6 performance within 10% of IPv4 when AS paths were the same
Only 63% of paths had similar performance when AS paths differed
79%
63%
IPv6 faster
IPv4 faster
Notes: slide 17: fix red and green (pick different colors)
annotated with numbers
(are lines on other graphs this thick?)
label blue line with what it is
add bullet to slide 17 about not-topology-matching paths
Performance differences between IPv4 and IPv6:
AS paths same: 79% of paths perform within 10%
AS paths differ: 63% of paths perform within 10%
less than half of paths of the same -- OF OUR SAMPLE!! #s in sample
red and green are bad colors to use next to eachother
anyuthing but green is better

## Slide 19: Relation between performance and AS-level paths
IPv6 performance is similar to IPv4 performance, if AS-level paths are the same
  Key finding of Nikkhah et al.
< 50% of AS paths from dual-stacked vantage points are currently the same in IPv4 and IPv6
Increasing congruence between IPv4 and IPv6 topology will improve performance and thus deployment incentives
M. Nikkhah, R. Guerin, Y. Lee, R. Woundy. Assessing IPv6 through web access: a measurement study and its findings. CoNEXT 2011.
Notes: ----- Meeting Notes (7/10/12 15:42) -----
too much text
title: "relation between performance and AS-paths"
say this in fewer words or a graph

## Slide 20: Potential AS-path congruence
For each link in an IPv4 AS path, is that link present in the IPv6 topology (anywhere)?
Based on links that already exist, up to 70% of paths could be identical (without building any new infrastructure)
Notes: slide 19: retrofit this workding back into slide 10b

## Slide 21: Potential AS-path congruence
For each AS in an IPv4 AS path, is that AS present in the IPv6 topology (anywhere)?
Based on ASes that are already in the IPv6 graph, more than 90% of paths could be identical
Notes: slide 20: did you talk to nanog
message seems about operators
make list of who should peer with who --> blog

## Slide 22: Routing Stability -- IIJ
Path exploration is similar in IPv4 and IPv6 since 2008
Time to convergence peaks in IPv6 are due to single prefix events -- convergence time is otherwise similar

## Slide 23: Summary of findings
The IPv6 network is maturing…albeit slowly and non-uniformly
The “core” of the network (transit providers) are mostly doing well with IPv6 deployment
The edge (enterprises and access providers) is lagging
IPv6 deployment is faster in Europe and Asia-Pacific regions, North America is lagging
IPv4 and IPv6 paths could potentially be 90% similar, without deploying any additional infrastructure

## Slide 24: Thanks! Questions?